Brad Nethercutt
20 June 2024

This document provides a description of all changes made to files within the DANCE_Simulation_G4.9 package in the effort to make it compatible with Geant4.10.01.2. With these changes, the simulation currently compiles and runs successfully in Geant4.10.01.2, and any apparent physics issues have been resolved. A benchmarking effort was performed to compare the DANCE simulation package running Geant4.9.3 versus Geant4.10.1.2 and the two versions were found to be in very good agreement.

DANCEEMPhysics.cc/.hh, DANCEHadronPhysics.cc/.hh:
substituted correct hadron and EM physics lists according to the tables below. The LowEnergy/LE and HighEnergy/HE models do not seem to be included with Geant4.10, so any references to these models have been replaced with the equivalent standard hadron/EM model, both in #include blocks at the top of the files as well as additional references which pop up throughout. Penelope models have a slight change to naming convention in G4.10, as shown in the table below.

DANCEHadronPhysics.cc:
substituted correct physics lists according to the table below, following the same steps as with DANCEEMPhysics.cc

DANCEEMPhysics.cc:
Commented out Low Energy pManager block, uncommented Standard EM pManager block

DANCEEventAction.cc:
- added “using namespace CLHEP;” to resolve errors claiming that some units were not declared in this scope
- Added histogram (f18) that shows energy deposition before any resolution is applied. This is useful for verifying that the gammas you expect to be there are actually there.

DANCEPrimaryGeneratorAction.cc:
- added “using namespace CLHEP;” to resolve errors claiming that some units were not declared in this scope
- Changed method of source definition. Use of the previous method caused gammas to be initialized with too much energy.

DANCEGeneralPhysics.cc:
changed instances of “theParticleIterator” to “aParticleIterator”. It appears this function, defined in G4VPhysicsConstructor.hh, changed name between G4.9 and G4.10.

GNUmakefile:
- Removed block which gave filepath for binmake.gmk and manually defined the correct filepath, based on the changes to .bashrc outlined below.
- Commented out definition of G4INSTALL. I defined this path in my .bashrc instead. G4 paths should be defined manually, as they will not carry over from a G4.9 installation correctly.

DANCEDetectorConstruction.cc:
- added “using namespace CLHEP;” to resolve errors claiming that units such as cm, g were not declared in this scope.
- Commented out unused material definitions (Teflon, Ti, Mylar, Gd, TargetMat, elLi,) as well as unused PMT_thick and PMT_curv. These materials generate a runtime null pointer error when defined but not used.

DANCEDetectorHit.cc
- added “using namespace CLHEP;” to resolve errors claiming that units MeV, ns were not declared in this scope.
src/B_crystal.hh:
- all instances of units deg and rad were changed to CLHEP::deg, CLHEP::rad to resolve errors claiming that these units were not declared in this scope. Adding “using namespace CLHEP” may also fix this issue.
include/C_crystal.hh:
all instances of units deg and rad were changed to CLHEP::deg, CLHEP::rad to resolve errors claiming that these units were not declared in this scope. Adding “using namespace CLHEP” may also fix this issue.

Directories are nested differently between installations of Geant4.9.3 and Geant4.10.1.2. Consequently, when the DANCE simulation package attempts to automatically set environment variables, they point to non-existent or incorrect directories. The following environment variables were written in .bashrc:
- Manually defined several environment variables which need to be given slightly different paths when using G4.10. These include:
  - G4INSTALL=/opt64/geant4/geant4-10.1.2/distribution
  - G4BASE=$(G4INSTALL)/source
  - G4LIB=/opt64/geant4/geant4-10.1.2/lib
  - G4INCLUDE=/opt64/geant4/geant4-10.1.2/include/Geant4
  - G4TMP=/user/path/to/DANCE_Simulation_G4.10/tmp
  - G4SYSTEM=Linux-g++
  Incorrect assumption of paths led to architecture.gmk trying to create these directories instead of successfully locating them.

To avoid “ERROR: MISSING LIBLIST OR LIBRARY MAP” during compilation: “source /opt64/geant4/geant4-10.1.2/share/Geant4-10.1.2/geant4make/geant4make.sh” before attempting to make DICEBOX_DANCE.

This table contains physics models that have been declared obsolete since G4.9 release, are not available in G4.10, and have designated replacements as documented in release/patch notes.
Models missing in Geant4.10 (comment out in DANCEHadronPhysics.cc/.hh or DANCEEMPhysics.cc/.hh)	Replacement models referenced in dev/release/patch notes (#include in DANCEHadronPhysics.cc/.hh or DANCEEMPhysics.cc/.hh)
G4LElastic	G4HadronElastic
G4LCapture	G4NeutronRadCapture
G4AntiProtonAnnihilationAtRest	Bertini or Fritiof models: G4AntiProtonAbsorptionFritiof?
G4MultipleScattering	G4eMultipleScattering
G4MultipleScattering	G4hMultipleScattering

This table contains physics models that are included in Geant4.9 but not available in the Geant4.10 distribution, as well as the best available replacement physics models I could find.
Models missing in Geant4.10 (comment out in DANCEHadronPhysics.cc/.hh or DANCEEMPhysics.cc/.hh)	Replacement models (#include in DANCEHadronPhysics.cc/.hh or DANCEEMPhysics.cc/.hh)
G4LEPionPlusInelastic	G4PionPlusInelasticProcess
G4LEPionMinusInelastic	G4PionMinusInelasticProcess
G4LEKaonPlusInelastic	G4KaonPlusInelasticProcess
G4LEKaonZeroSInelastic	G4KaonZeroSInelasticProcess
G4LEKaonZeroLInelastic	G4KaonZeroLInelasticProcess
G4LEKaonMinusInelastic	G4KaonMinusInelasticProcess
G4LEProtonInelastic	G4ProtonInelasticProcess
G4LEAntiProtonInelastic	G4AntiProtonInelasticProcess
G4LENeutronInelastic	G4NeutronInelasticProcess
G4LEAntiNeutronInelastic	G4AntiNeutronInelasticProcess
G4LELambdaInelastic	G4LambdaInelasticProcess
G4LEAntiLambdaInelastic	G4AntiLambdaInelasticProcess
G4LESigmaPlusInelastic	G4SigmaPlusInelasticProcess
G4LESigmaMinusInelastic	G4SigmaMinusInelasticProcess
G4LEAntiSigmaPlusInelastic	G4AntiSigmaPlusInelasticProcess
G4LEAntiSigmaMinusInelastic	G4AntiSigmaMinusInelasticProcess
G4LEXiZeroInelastic	G4XiZeroInelasticProcess
G4LEXiMinusInelastic	G4XiMinusInelasticProcess
G4LEAntiXiZeroInelastic	G4AntiXiZeroInelasticProcess
G4LEAntiXiMinusInelastic	G4AntiXiMinusInelasticProcess
G4LEDeuteronInelastic	G4DeuteronInelasticProcess
G4LETritonInelastic	G4TritonInelasticProcess
G4LEAlphaInelastic	G4AlphaInelasticProcess
G4LEOmegaMinusInelastic	G4OmegaMinusInelasticProcess
G4LEAntiOmegaMinusInelastic	G4AntiOmegaMinusInelasticProcess
G4HEPionPlusInelastic	HE physics model replacements are just the standard ones already listed above.
G4HEPionMinusInelastic
G4HEKaonPlusInelastic
G4HEKaonZeroInelastic
G4HEKaonMinusInelastic
G4HEProtonInelastic
G4HEAntiProtonInelastic
G4HENeutronInelastic
G4HEAntiNeutronInelastic
G4HELambdaInelastic
G4HEAntiLambdaInelastic
G4HESigmaPlusInelastic
G4HESigmaMinusInelastic
G4HEAntiSigmaPlusInelastic
G4HEAntiSigmaMinusInelastic
G4HEXiZeroInelastic
G4HEXiMinusInelastic
G4HEAntiXiZeroInelastic
G4HEAntiXiMinusInelastic
G4HEOmegaMinusInelastic
G4HEAntiOmegaMinusInelastic
G4hLowEnergyIonisation	G4hIonisation
G4LowEnergyRayleigh	G4RayleighScattering
G4PenelopeCompton	G4PenelopeComptonModel
G4PenelopeGammaConversion	G4PenelopeGammaConversionModel
G4PenelopePhotoElectric	G4PenelopePhotoElectricModel
G4PenelopeIonisation	G4PenelopeIonisationModel
G4PenelopeBremsstrahlung	G4PenelopeBremsstrahlungModel
G4PenelopeAnnihilation	G4PenelopeAnnihilationModel
G4LowEnergyPhotoElectric	G4PhotoElectricEffect
G4LowEnergyCompton	G4ComptonScattering
G4LowEnergyGammaConversion	G4GammaConversion
G4LowEnergyIonisation	G4eIonisation
G4LowEnergyBremsstrahlung	G4eBremsstrahlung